## Slide 1: ダイナミックレンジの大きな 電荷有感型前置増幅器の開発
M. Kurokawaa), H. Babaa), T. Gunjib), H. Hamagakib),
S. Hayashib),T. Motobayashia), H. Murakamia), A. Taketania),
M. Tanakac), Y. Toganoa), K. Yonedaa)
a) RIKEN, Nishina Center
b) CNS, the Univ. of Tokyo
c) KEK

## Slide 2: 大きなダイナミックレンジが必要となる原子核実験 （中間エネルギー領域）
Coulomb breakup exp.（陽子捕獲反応の逆反応）
proton
heavy particle
(z < 50)
Dynamic range of the electronics ~ 10^4
  coincident measurement from proton (z = 1) to heavy ions (z ~ 50)  2500
  Pileup of beam events
proton rich particle up to 10050Sn
Definition of dynamic range
upper limit / lower limit (= 4s)
of detection
Nuclear decay spectroscopy
Implantation > GeV
b decay > a few tens of keV

## Slide 3: これまでに開発が行われた回路の例
このレベルに応じて
瞬時に切り替える
I.
II.
Ref.) M.A. Baturisky, et al., Nucl. Instr.and Meth.
A 496 (2003) 162 – 171.
Ref.) V. Bonvicini, et al., Nucl. Instr.and Meth.
A 572 (2007) 340 – 344.  10000 MIP 実現 S/N = 5 for 1 MIP
Ref.) D. Braga, et al., IEEE NSS-MIC 2009
Conf. Rec., 1924 – 1928.
III. TOT

## Slide 4: Architectures of the present ASIC
Cf = 1.8 pF
Rf = 50 MW equivalent: Krummenacher feed back circuit is used ref.) F. Krummenacher, Nucl. Instru. Meth., A305 (1991) 527.
Power consumption 10 mW/ch
Capacitive division
Openloop gain
Saturation suppression

## Slide 5: Architecture I: dual channel system
Input charge is divided in proportion to the capacitance ratio between coupling capacitances Ch and Cl (Ch > Cl).
Ref. ) N. Uematsu and S. Nishimura, “Development of silicon strip detector with wide-dynamic-range readout system from
20 keV to 4 GeV”, RIKEN Accel. Prog. Rep. 41, (2008) 151.
CSA
CSA
Qin
Ch
Cl
Qh = Qin × Ch / (Ch + Cl)
Ql = Qin × Cl / (Ch + Cl)
Log Qin
Log Vout
4 pC
40 pC
high-gain
channel
low-gain
channel
Extended as much as the
capacitance ratio
Ch = 10 × Cl
H
L
similar response with
single channel system

## Slide 6: Architecture II: cascode current mirror for the achievement of ideal A
At rising edge of the pulse, Zin = 1 / (A Cf s)
A: open loop gain
To divide the input charge in proportion to the capacitance ratio, input impedance of the CSA has to be negligible small.  A = ∞ is ideal
 ideal current source
Cascode current mirror is employed. It has the similar structure with HINP16C to reduce the voltage drop.
Equivalent circuit for the dual channel system
ZCh
ZCl
Zin
Zin
w/l--> small
w/l--> large
w/l--> small
w/l--> large
w/l--> large
w/l--> small
input
Cacode current mirror
LogHz
LogA
50 dB
80 dB

## Slide 7: Architecture III: saturation suppression
Log Qin
Log Vout
If Qin is large enough to saturate the high-gain channel,,,,,,,
Z of the CSA for the high-gain channel is quite large!
Charge flows into low-gain channel.
Capacitive division does not work there.
Saturation suppression for the high-gain channel is implemented.
Vg
Charge flows into this FET,
becauce of its small drain-source resistance.
CSA
H
L
This FET is turned ON when Vth > Vg - Vout
Vout

## Slide 8: Output pulse shapes from the CSAs
Ch
Cl
CSA
CSA
This part is implemented in first prototype
Chip and its test board TSMC 0.5 mm process chip size ~ 1.6 mm × 1.2 mm
H
L

## Slide 9: Output pulse shapes from the CSAs -- I
Qin = 3.2 pF (FET is Off)
100 nsec/div
1
1 /( Ch s)
Ch = 560 pF
Cl = 56 pF
Ch = 4.7 nF
Cl = 470 pF
L
H
H
L
100 nsec/div
10
I
1 /( Cl s)
R
(=Zin)
Impedance of each ch.
Rise time is a function of Cin, Ch, Cl and Zin and depends on √(Cin2 (1 / Ch – 1 / Cl)2 + 4)
Usually is a funcionf Cin & Zin

## Slide 10: Output pulse shapes from the CSAs -- II
Qin = 16 pF (FET is On)
Saturation suppression is working.
Shape shows plateau,
but not due to the saturation.
off / on/ off
Zin  source-drain resistance of the FET
Anyway, the effect of the bumps will be filtered by subsequent analysis
with t ~ 1 ms.
Ch = 560 pF
Cl = 56 pF
Ch = 4.7 nF
Cl = 470 pF

## Slide 11: Result I: Dynamic range for a single channel CSA
ADC-H
ADC-L
10-3
10-2
10-1
100
101
102
100
101
102
103
104
5.2 fc
5.6 pc
Definition of lower limit = 4s. 4.4 fC corresponds to 100 keV.
Dynamic range ~ 10^3

## Slide 12: Result II: Dynamic range for dual channel CSAs
10-3
10-2
10-1
100
101
102
100
101
102
103
104
ADC-H-H
ADC-H-L
ADC-L
5.8 fc
56 pc
Definition of lower limit = 4s
Dynamic range ~ 10^4
10 times wider than that is obtained
for the single channel usage

## Slide 13: Example of the modification using FIB@RIKEN
Disconnection of traces
passivating coating
Insulation layer
Metal (Al) layer
enlarged and tilted view
Limited area was irradiated with
Ga beam
RIKENDGCSP

## Slide 14: Summary
First prototype of RIKENDGCSP (Riken Dual Gain Charge Sensitive Preamplifier) is working well. Dynamic range can be extended as much as the gain ratio.
Second prototype is now under fabrication
CSA
電流量：
エミッターフォロアー
の電流量で決まる
CSA